## Slide 1
Scripts for Hack5 tools

## Slide 2
Screen Crab
Presented by Miłosz Obrębski

## Slide 3
Screen Crab is a hacking tool developed by Hak5. Designed to appear as a harmless video adapter or dongle. It functions as an man-in-the-middle video proxy.
The device sits between the source device and the monitor, it allows for screen capture recording, remote live streaming of visual data over Wi-Fi, and spying on a target's on-screen activity without triggering any operating system alerts.
What the PC sees
Reality
Normal monitor
Evil proxy

## Slide 4
Use cases:
- Remote grabbing of sensitive data
- Remote control when paired with for example Key Croc
- Recording videos
Author of this presentation is not responsible for any non educational use cases, only use the device within the law

## Slide 5
Configuration
How to make it work?

## Slide 6
Screen crab after boot loads config file from the sd card. The most important thing is to configure the wi-fi, other settings were left as they were

## Slide 7
C2 Cloud
Dedicated management solution
for hak5 devices

## Slide 9
C2 Cloud interface allows:
- to configure the devices without using the sd
- to collect loot
- to remotely access target computer
- to read logs
- to see statistics eg. uptime
To add a device the device.config file is placed in the root directory of the device. This file is generated from the dashboard
C2 cloud is meant to be self-hosted on a public server which the Hak5 device can access

## Slide 10
The script
Student id grabber

## Slide 11
The script is written in python and uses api of C2 Cloud to fetch and process images
The main feature of the script is stealthily saving screenshots of student ids on pg login website.
Images are taken by default every 10s, the script downloads latest one and uses opencv to detect logo of PG to detect if the user is on the login website.
It is very easy to modify the search image

## Slide 12
First we need to connect the device to the target computer. Video output from PC goes to Screen Crab and output of screen crab goes to the monitor
What the PC sees
Reality
Normal monitor
Evil proxy

## Slide 14
Once PG logo was detected in the image the script saved that image to disk for further analisis

## Slide 15
THE END
Screen Crab
Presented by Miłosz Obrębski